## Slide 1: Chhaya: the diabetes digital twin that keeps going when the sensor is off
HAPPIEST HEALTH DIGITAL TWIN CHALLENGE 2026 · TEAM SYNAPSEX · D.B.S KANPUR
It fuses a patient’s health record with a wearable glucose sensor, draws an honest band around every estimate, says when its report may be out of date, and proves every claim on patients it never saw.
DAY 1
DAY 2
DAY 3
DAY 4
DAY 5
DAY 6
typical day, 5 days folded
SENSOR ON
THE SHADOW, ESTIMATED
THE SENSOR, REVEALED (SIMULATED)
PROMPT ON DAY 6
180 mg/dL
70
estimate (the shadow)
80 % band
sensor, revealed
fingerstick
meal
Mrs. R. is a synthetic demo patient and the sensor shown is simulated. Research prototype, not a medical device.
Notes: Chhaya means shadow. When a patient takes the sensor off, our twin keeps estimating glucose, always drawn with an honest band, and it says when its report may be out of date. The chart is the twin’s own output for a synthetic demo patient: the purple shadow, the teal sensor revealed over it, the pink fingersticks, and the prompt that fires on day six. Everything on the next nine slides was scored once on patients the model never saw.

## Slide 2: One sensor wear, then months of decisions on an ageing report
101 million
people in India live with diabetes
ICMR-INDIAB national study, 2023
₹4,400–5,100
for one 14-day glucose-sensor wear
Indian retail listings, October 2026
26 sensors
a year to wear one continuously: over ₹1.1 lakh
26 times the lowest listed price
THE SCENARIO
14 days of sensor data
Months of treatment decisions made from that one report
?
Nobody tells the doctor how old that report has become.
Sources: ICMR-INDIAB national cross-sectional study, The Lancet Diabetes & Endocrinology, 2023 (101 million, 11.4 %). Retail listings checked on 11 October 2026 (Truemeds; Amazon India price history); prices vary by model and seller.
Notes: India has about 101 million people with diabetes. A 14-day glucose sensor costs roughly 4,400 to 5,100 rupees at retail, so wearing one continuously would take 26 sensors a year, more than 1.1 lakh rupees. A realistic pattern is one wear, then months of treatment on that report, and nobody tells the doctor how old the report has become. That gap is what Chhaya addresses.

## Slide 3: Two streams fused into one personal twin, checked against the brief
Health record
static · FHIR-shaped
+
Sensor, meals, band, fingersticks
dynamic
→
Twin
shadow with an 80 % band
→
Gate
scored once, unseen patients
→
Doctor’s screen
three screens, offline
1
Static stream
A FHIR-shaped health record: diagnosis, duration, HbA1c, fasting glucose, BMI, medications.
2
Dynamic stream
CGM sensor wear, meal log, wrist-band activity and fingersticks.
3
Fusion
The record sets the prior; the sensor wear is the evidence (MAP fit, Laplace ensemble).
4
Adverse events predicted
Post-meal excursion (AUROC 0.82 with the sensor, 0.71 without) and a stale-report prompt (AUROC 0.82).
5
Doctor dashboard
One panel per stream plus the shadow; runs offline; live demo online.
Notes: This is the whole system in one line, and the five numbers are the challenge brief. One: a static health record. Two: dynamic streams from the sensor, meals, wrist band and fingersticks. Three: they are fused, the record sets the prior and the sensor wear is the evidence. Four: the adverse events we predict are the post-meal excursion and a stale-report prompt. Five: a doctor dashboard. Between the twin and the doctor sits a gate that every claim had to pass.

## Slide 4: A physiology-based twin, fitted to one wear and always drawn with its uncertainty
1
Record
Fasting glucose sets the prior
→
2
Wear
MAP fit from six starts
→
3
Ensemble
Laplace posterior, 200 members
→
4
Simulate
E-DES, RK4, JAX float64
→
5
Blend and nudge
Half own day; fingerstick fade 120 min
→
6
Output
Shadow, 80 % band, CUSUM prompt
THE PHYSIOLOGY: E-DES, MAAS ET AL. 2015
Gut
Plasma glucose
Interstitial fluid
Plasma insulin
what the sensor reads
meals
circadian term
plus an exercise term on uptake
Seven personal parameters per patient
METHOD FACTS
No neural network, no pretrained model, no large language model
Seven personal parameters fitted per patient from one wear
Fingerstick filter fades over 120 minutes; CUSUM raises the drift prompt
Python 3.12 · JAX · SciPy · scikit-learn · FHIR-shaped record
Notes: The twin is a physiology model, E-DES, with a circadian term and an exercise term, integrated with a fourth-order Runge-Kutta scheme in JAX at float64. The health record sets a prior on basal glucose; the sensor wear is the evidence; a MAP fit from six starts gives the personal parameters and a Laplace posterior gives a 200-member ensemble, which produces the 80 percent band. The estimate is half physiology and half the patient’s own average day. Fingersticks nudge it and fade over two hours, and a CUSUM on fingerstick surprises raises the drift prompt. There is no neural network, no pretrained model and no language model anywhere in the system.

## Slide 5: The doctor sees one panel per stream, plus the shadow
Clinic list
Patient
Evidence
Mrs. R. · synthetic demo patient
From the health record
record prior
Type 2 diabetes mellitus · duration 9 years
HbA1c 8.1 % · fasting glucose 137 mg/dL
Today’s shadow
estimated
Fingersticks
as read
36 since the sensor, 6.0 a day
Meal excursion history
sensor wear
Breakfast 5 of 5
100 %
Lunch 5 of 5
100 %
Dinner 5 of 5
100 %
Snack 3 of 5
60 %
From the health record
The record sets the twin’s prior. With sensor data, the sensor dominates.
Meal excursion history
How often each meal type was followed by a reading above 180 mg/dL within two hours during the wear. A description, not a forecast.
Reveal
Hide the sensor, estimate, then slide the real trace over the shadow and see where it was right and where it missed.
Try it: chhaya-digital-twin.vercel.app
Notes: This is the patient screen, drawn from the demo bundle for our synthetic patient. The health record panel shows what sets the twin’s prior. The shadow is the estimate with its band. Fingersticks are shown as read from the meter. The meal excursion history describes, from the sensor wear only, how often each meal type was followed by a reading above 180 within two hours; it is a description and not a forecast. And the reveal lets the doctor see where the shadow was right and where it was not. The live demo is online.

## Slide 6: With the sensor on, the spike is predictable; with it off, more streams do not help
Chart: Post-meal excursion, AUROC by what the model is given (axis starts at chance, 0.5)
| Record only | Fingersticks only | Sensor week only | Fused, sensor off | Sensor on (reference)
AUROC | 0.646 | 0.703 | 0.777 | 0.713 | 0.816
0.82 · 0.76
AUROC · AUPRC with a live sensor
0.71 · 0.60
AUROC · AUPRC, fused, sensor off
8.9
false alerts per patient-week, so no alert is shown
Four other fusion strategies (equal-weight, stacked, recalibrated, stronger regularisation) were tried on development patients: none beat a single stream.
47 held-out ShanghaiT2DM patients, 1,205 meals, 39 % followed by an excursion. Event: two consecutive readings above 180 mg/dL within 2 hours of a meal start. Exploratory fusion benchmark: 1,436 meals, 49 development patients, patient-grouped cross-validation.
Notes: This is the brief’s own example: predicting a glucose spike in advance. At the moment a meal starts, with the live sensor on, the model reaches an AUROC of 0.82. Take the sensor off and the fused model drops to 0.71, and adding streams does not buy it back: the fused model sits below the sensor week alone. We also tried four other fusion strategies on the development patients and none beat a single stream. At 8.9 false alerts per patient-week the model is not usable as an alert, so the dashboard shows no alert and no probability.

## Slide 7: Every claim crossed a gate: bars written first, scored once on unseen patients
5 passed · 4 missed · all nine published
Half of every cohort tunes the model; the other half is scored once.
The confirmatory command needs --confirm and refuses a second run.
95 % intervals come from a bootstrap over patients (2,000 resamples).
Every claim on the Evidence screen is tested word for word against a decision record.
Shadow: closer than the average day
PASSED
1.4 mg/dL, small
Fingersticks keep the report truer
PASSED
at about six a day
Prompt flags a stale report
DESCRIPTIVE
AUROC 0.82
Record improves the estimate
MISSED no detectable gain
×
stopped at the gate
A fused-model alert is usable
MISSED slope 0.48; 8.9 false alerts per patient-week
×
stopped at the gate
What the misses changed in the product: no meal alert and no probability. The dashboard shows the patient’s own excursion history instead.
Notes: Nine bars were written before any run: five passed and four missed, and all nine are published. Half of every cohort tunes the model and the other half is scored exactly once; the command refuses a second run. Three claims crossed the gate and two were stopped: the record did not improve the estimate, and a fused-model alert was not usable. The misses changed the product: there is no meal alert and no probability, and the dashboard shows the patient’s own recorded excursion history instead.

## Slide 8: Three results a clinician can use, each with its conditions
A FINGERSTICK-ANCHORED REPORT
13.0 → 6.4
mg/dL median error
stale report
plain fingerstick average
Error of the next days’ mean sensor glucose, in hindsight.
29 held-out patients, supervised care, about six fingersticks a day. At one a day the gain was 0.3 mg/dL.
WHICH LOWS NOT TO TRUST
8 of 64
sensor lows confirmed by a fingerstick
None of the 9 night-time lows was confirmed. Unconfirmed is not the same as false.
Readings below 70 mg/dL with a fingerstick within 10 minutes. Descriptive, no bar.
A PROMPT, NOT A FINDING
0.82
AUROC for a drifted sensor report (0.63 to 0.98)
7 of 11 drifted recordings raised it
2 of 21 stable recordings raised it
A running sum of fingerstick surprises. A plain comparison does as well (0.82).
32 held-out recordings, supervised care.
Notes: Three results a doctor can use. First, with about six fingersticks a day in supervised care, the error of the report against the next days’ mean sensor glucose falls from 13.0 to 6.4 milligrams per deciliter; at one fingerstick a day the gain was only 0.3. Second, of 64 sensor lows that had a fingerstick within ten minutes, only 8 were confirmed, and none of the 9 at night; unconfirmed is not the same as false. Third, a simple running sum of fingerstick surprises flags a drifted report with an AUROC of 0.82, but a plain comparison does as well, so it is shown as a prompt, never as a finding.

## Slide 9: Honest limits, and what Indian validation would take
LIMITS
No Indian patient data. The evidence is a supervised-care cohort (ShanghaiT2DM) and a free-living cohort of mixed glycaemic status (CGMacros).
Small effects. The shadow is 1.4 mg/dL closer than the patient’s own average day; the physiology alone beats it in only 60 % of held-out patients.
Conditional gains. The fingerstick result holds at about six a day in supervised care.
Research prototype. No dose advice, no low-glucose estimates, no alarms.
ROADMAP
1
Now
Open-data prototype: nine pre-registered bars, five passed, every number reproducible.
2
Next
An Indian clinic cohort, outpatient fingerstick frequencies of one or two a day, bars written before the run.
3
Then
A prospective check that the stale-report prompt changes a clinical decision.
Notes: We would rather show the limits than have you find them. There is no Indian patient data in the evidence; it is a supervised-care cohort and a free-living cohort of mixed glycaemic status. The effects are small. The fingerstick gain holds at about six a day in supervised care. And this is a research prototype with no dose advice, no low-glucose estimates and no alarms. Indian validation would mean a clinic cohort, outpatient fingerstick frequencies of one or two a day, and bars written before the run, then a prospective check that the prompt changes a decision.

## Slide 10: Every number is a command
Chhaya means shadow. When the sensor goes, the twin stays, and it says when to stop trusting it.
LIVE DEMO
chhaya-digital-twin.vercel.app
CODE
github.com/AdityaChandel11/DigitalTwinHack
REPRODUCE
uv sync
uv run python -m chhaya.dashboard
uv run pytest -q
400+ tests · 15 decision records · pre-registered bars · code MIT, data CC BY 4.0 and CC BY-NC-SA 4.0
Scan to open the demo
Team SynapseX
D.B.S. College, Kanpur
Notes: Everything you have seen is reproducible. The live demo is online, the code is public under the MIT licence, and three commands reinstall the environment, start the dashboard and run the test suite. The datasets keep their own licences and are never redistributed. Chhaya means shadow: when the sensor goes, the twin stays, and it tells you when to stop trusting it. Thank you.